## Slide 1: SRAM Only Mode
Other Memory (Flash / DRAM)
not used
Ethos-U
SRAM
const_mem_area arena_mem_area
Cortex-M CPU
Shared SRAM Mode
Other Memory (Flash / DRAM)
const_mem_area
Ethos-U
SRAM
arena_mem_area
Cortex-M CPU
Dedicated SRAM Mode
Other Memory (Flash / DRAM)
const_mem_area arena_mem_area
Ethos-U
SRAM
cache_mem_area
Cortex-M CPU
Prefetch weights
Prefetch weights

## Slide 2: Ethos-U Optimized Software Flow for Tensorflow/PyTorch
HOST (OFFLINE)
github.com/Arm-Examples#edge-ai-and-machine-learning
DEVICE with Ethos-U
CMSIS-NN
Optimized Kernels
Cortex-M
CPU
Ethos-U Driver
Vela Compiler
Ethos-U NPU
ML Runtime
Optimized ML Model
Quantized ML Model
Ethos-U target system & memory description
Notes: ML models from ecosystem partners or open-source model zoos such as Hugging Face are quantized and optimized for embedded deployment. CMSIS-NN executes these optimized models on Cortex-M processors. For Ethos-U NPU targets, Vela converts model operations for NPU acceleration, while operations that cannot be converted continue to run on Cortex-M via CMSIS-NN.
Using these workflows, developers can deploy trained models from PyTorch, TensorFlow, and other frameworks onto Arm targets with optimal performance and energy efficiency, enabling intelligent capabilities in IoT devices, wearables, industrial sensors, and other edge computing applications.

## Slide 4: Ethos-U Optimized Software Flow for Tensorflow/PyTorch
github.com/Arm-Examples#edge-ai-and-machine-learning
DEVICE with Ethos-U
CMSIS-NN
Optimized Kernels
Cortex-M
CPU
Ethos-U Driver
Ethos-U NPU
ML Runtime
Optimized ML Model
DEVICE without Ethos-U
CMSIS-NN
Optimized Kernels
Cortex-M
CPU
ML Runtime
Optimized ML Model
Notes: ML models from ecosystem partners or open-source model zoos such as Hugging Face are quantized and optimized for embedded deployment. CMSIS-NN executes these optimized models on Cortex-M processors. For Ethos-U NPU targets, Vela converts model operations for NPU acceleration, while operations that cannot be converted continue to run on Cortex-M via CMSIS-NN.
Using these workflows, developers can deploy trained models from PyTorch, TensorFlow, and other frameworks onto Arm targets with optimal performance and energy efficiency, enabling intelligent capabilities in IoT devices, wearables, industrial sensors, and other edge computing applications.